## Slide 2
Agenda
introduction to Forecast
Importance of Forecast
Develop A Simple Forecast

## Slide 3
Forecasting
Forecasting is the process of making predictions of the future value, based on past and present data. Most commonly by analysis of trends. A common example might be estimation of some variable of interest (e.g. Electricity Consumption) at some specified future date.

## Slide 4
LOAD FORECASTING
  “ Load Forecast is the 1st and the foremost step of planning on which the investment in generation, transmission and Distribution is based ”

## Slide 5
WHAT DO WE FORECAST?
Everything ?
Weather Forecast
          Rain - Wind velocity
          Temperature - Humidity
Production Forecast
          Sale - Supplies
          Demand - Costs
Agriculture Forecast
      Demand - Imports Estimate
Fuel Forecast
    Requirement -LNG, Crude Oil - Import
    5. Stock Market Shares Forecast

## Slide 6: Why Forecast is important
Augmentation in a grid requires two years
Construction of new grid requires three years
Construction of a Transmission line also takes ample time
In future DISCOs may have to assess generation requirements
These functions should be carried out at appropriate time which can not be possible without realistic forecast
For all the above heavy investment is required (If forecast is not realistic it will lead to heavy debit or load shedding)

## Slide 7
Load Forecasting
Generation Expansion Planning
Transmission Expansion Planning
Environmental Analysis
Economic/Financial Analysis
Investment Plan
Final Expansion Plan
Importance of Forecast In POWER PLANNING PROCESS
Feasible
Not Feasible

## Slide 8: Developing A Simple Forecast

## Slide 9: Terms Used In Developing An Energy & Demand Forecast
Consumption
AACGR (Growth Rate)
Distribution Losses (Difference Between % and Actual Number)
Transmission Losses
Energy Sent out
Load Factor
Peak Demand
Base Year
Losses Reduction Plan (Projection of Losses)

## Slide 11
Network Design Diagram

## Slide 12
Historical Sale of LESCO
Financial Total Sale
n Year (GWh)
1 2014 15948
2 2015 16328
3 2016 17342
4 2017 17782
5 2018 20448
AACGR 6.41
Please Make A Projection Of 2018 Sale Using 5% Growth Rate For Next Five Years.

## Slide 13
Make Projection of Each Category From Excel Sheet

## Slide 15
Year | Energy Sale |  | Distribution Losses |  | Energy Received at 11 kV | Peak Demand at 11 kV | Transmission Losses |  | Energy Sent out at 132 kV | Load Factor | Peak Demand at 132 kV
 | (GWh) | G.R | (GWh) | (%) | GWh | MW | (GWh) | (%) | (GWh) | (%) | (MW)
2017-18 | 20448 |  | 3046 | 12.96 | 23495 | 3822 | 237 | 1.00 | 23731 | 70.2 | 3861
2018-19 | 21621 | 5.7 | 3173 | 12.80 | 24794 | 4130 | 248 | 0.99 | 25042 | 68.5 | 4172
2019-20 | 23316 | 7.8 | 3311 | 12.43 | 26627 | 4479 | 264 | 0.98 | 26890 | 67.9 | 4524
2020-21 | 24952 | 7.0 | 3451 | 12.15 | 28403 | 4810 | 278 | 0.97 | 28681 | 67.4 | 4857
2021-22 | 26514 | 6.3 | 3623 | 12.02 | 30137 | 5133 | 292 | 0.96 | 30429 | 67.0 | 5183
2022-23 | 28197 | 6.4 | 3811 | 11.91 | 32009 | 5448 | 307 | 0.95 | 32316 | 67.1 | 5500
2023-24 | 29827 | 5.8 | 4016 | 11.87 | 33844 | 5802 | 322 | 0.94 | 34165 | 66.6 | 5858
2024-25 | 31576 | 5.9 | 4241 | 11.84 | 35817 | 6186 | 337 | 0.93 | 36154 | 66.1 | 6244
2025-26 | 33410 | 5.8 | 4475 | 11.81 | 37885 | 6593 | 352 | 0.92 | 38237 | 65.6 | 6655
2026-27 | 35184 | 5.3 | 4736 | 11.86 | 39920 | 7001 | 367 | 0.91 | 40287 | 65.1 | 7065
2027-28 | 37034 | 5.3 | 4936 | 11.76 | 41970 | 7360 | 382 | 0.90 | 42352 | 65.1 | 7427
Ave. Growth (2018-2028) | 6.12% |  |  |  | 5.97% | 6.77% |  |  | 5.96% |  | 6.76%
LESCO Forecast without incorporating Load Shedding effect (Low Forecast)

## Slide 16
I Step : Complete Base Year Figures
II Step : Adding Distribution Losses (%)
III Step : Adding Transmission Losses (%)
IV Step : making Total Losses (%)
V Step : Calculating Energy Sent out
VI Step : Applying Load Factor
VII Step : Calculating Peak Demand
Steps In Developing Simple Forecast